## Slide 1
SDU Summer School - Medical Robotics
Team Potato Pokers
Christian W. Bundschu, Julia Rey Vilches, Jaeseung Byun, Daniel Schober

## Slide 2
Introduction
Christian Bundschu Ph.D. Candidate - Mechanical Engineering
Julia Rey Vilches M.S. Student - Autonomous Systems
Jaeseung Byun Ph.D. Candidate - Mechanical Engineering
Daniel Schober M.S. Student – Autonomous Systems
Team Members

## Slide 3
Objectives
Teach a robot arm to perform an electrical impedance measurement procedure autonomously:
  Using robot learning by demonstration
  Conductivity mapping
Encode the learned trajectory using dynamic movement primitives
  Generalized for multiple probing locations
Object detection in a pool of ionized water (salted) using electrical impedance detection for the following:
  No object
  Conductive object
  Non-conductive object
Explore the potential for object mapping via experimental procedure
Experiment Targets

## Slide 4
Principles
Tripolar configuration
Object Detection via Conductivity
Target Object
Impedance
, the same for

## Slide 5
Principles
Second-order system forced upon by a disturbance term onto a trajectory
Learn the weights of the force function via Gaussian basis functions
One-shot learning
                We only have to show the movement to the robot once
          We can use different initial and goal points
  We can scale the speed of the motion using Tau
Assumptions
  Fixed constants of alpha and beta are being used, assuming the M C K of the second order system remain constant (critically damped)
  Uniformly spaced distances
Explore the potential for object mapping via experimental procedure
Dynamic Movement Primitives
L
L
L
Demonstration
DMP
Demonstration
DMP
L
2L
Learning by demonstration (Manual Guidance)

## Slide 6
Principles
L
L
L
Demonstration
DMP
Demonstration
DMP
L
2L
DMP Result
Trajectory map
10 mm

## Slide 7
Experiment Set-Up
6-DOF Robot Arm - Universal Robotics UR3
Eliko QuadraTM Impedance Spectroscopy
Salter water bath
Cylindrical aluminum and plastic objects
Davinchi probes (input current and signal)
  Probe is dipped 1mm
  10mm between points
Tri-polar configuration
Equipment & Parameters

## Slide 8
Demo Video

## Slide 9
Results
Ecoflex 30 Skin (~20mm thick)
Sensor Joint (100kg loadcell)
Mannequin Core
Water
Conductivity is constant except when the probe is too close to the charge cloud
Plastic
Conductivity is lower than water but also relatively constant over object surface
Metal
Conductivity is clearly higher over the object
Experiment Targets

## Slide 10
Conductivity
Results are accurate if:
          The probe is too deep in the water
          The distance between the target & surface is too far away
DMPs
Overall DMP shape tracks the initial and goal points
Demonstration trajectory is not preserved if:
    Distances are different
    Orientations are different
Reformulating DMPs to preserve MCK can fix the issue
Discussion & Conclusion
Avalanche search and rescue
Lochness monster search and destroy
Submarine Espionage
Discussion
Possible applications

## Slide 11
Thank You
고맙습니다